## Slide 1: Electronics & Electricity
Unit 2 – Electric Circuits and Devices
Section 1 – Circuits, Voltage, and Current

## Slide 2: Electric Circuits and Devices
Circuits, Voltage, and Current

## Slide 3: Google classroom code
1c62ger

## Slide 4: The big idea
Ability to sketch a basic circuit and identify its four parts
Explain differences between series, parallel, and series-parallel circuits
Define voltage and current
Difference between direct current (DC) and alternating current (AC)
Explain sine waves

## Slide 5: Terms
Alternating current
Ampere
Conductor
Current
Cycle
Direct Current
Electric Circuit
Load
Parallel circuit
Series circuit
Voltage

## Slide 6: Parts of a circuit
An electric circuit is a combination of parts connected to form a complete path through which electrons move
A basic complete circuit has four parts:
The energy source
The conductors
The load
The control device

## Slide 8: Energy Source
Produces the force that causes electrons to move
Acts like a water pump pushing water through a pipe
The FORCE is called voltage
Electrons are negatively charged so they are attracted by positive charges
Electrons flow from negatively charged object to the positive object
The FLOW of electrons is called current

## Slide 10: Conductors
Conductors in a circuit provide an easy path through which electrons can move
Copper is the most commonly used conductor material
  Copper wire might be bare or covered with some kind of insulating material

## Slide 11: Load
Part of a circuit that changes the energy moving electrons into some other useful form of energy
  Common load is that of a light bulb
Loads can be connected in series or parallel

## Slide 12: In series
Provides only one path, or one loop

## Slide 13: In parallel
There may be two or more different paths, or loops through which electrons flow

## Slide 14: Control Device
Your typical control device is a wall on-off switch
It opens and closes a circuit
Acts as a conductor when on to keep electrons flowing
  The circuit is said to be CLOSED
When off, the circuit path is interrupted and electrons can no longer flow
  The circuit is said to be OPEN

## Slide 15: Voltage
The charge (electron) “pusher.”
Voltage causes current to flow/move.
Voltage sources:
  Battery
  Generator
  Outlets
Symbol for voltage = V
Unit for voltage = Volts (V)

## Slide 16: Alessandro Volta (1745 – 1827)
Italian physicist
known especially for the invention of the electrochemical cell, aka the battery in 1800.

## Slide 17: Voltage At Home
Power utilities use large generators to provide the 120V that is delivered to your home outlets.
When you plug in something to the outlet (lamp, blow dryer, TV, etc) the voltage is applied across the circuit, allowing the charge to flow (electric current).

## Slide 18: Current
Current: flow of charge (electrons) within a conductor or how fast charge is moving.
Charge will only flow if there is a voltage source (potential difference).
Symbol for Current = I
Unit for Current = Amps (A)

## Slide 19: André Ampère (1775 – 1836)
French physicist and mathematician.
One of the main discoverers of electromagnetism.
SI unit of measurement of electric current, the ampere, is named after him.

## Slide 20: Resistance
Resistance: opposes the push from the voltage source. Resistance affects the speed of the current.
Symbol for Resistance = R
Unit for Resistance = Ohms (Ώ)