## Slide 1: Electronics & Electricity
Unit 5 – parallel Circuits
Section 1 – parallel Circuits

## Slide 2: Parallel Circuits
Parallel Circuits

## Slide 3: The big idea
Ability to draw and label a parallel circuit and indicate the polarity at each resistor
Define the term overloaded circuit
Use the three parallel-resistance formulas
Calculate the equivalent resistance of a parallel circuit
Calculate the total resistance, the total current, and the branch current in a parallel circuit\
Connect batteries in parallel to increase current capacity

## Slide 4: Terms
Booster battery
Branch circuit
Equivalent resistance
Kirchoff’s current law
Overload
Parallel circuit
Shunt connection
Total current

## Slide 5: Parts of a circuit
An electric circuit is a combination of parts connected to form a complete path through which electrons move
A basic complete circuit has four parts:
The energy source
The conductors
The load
The control device

## Slide 6: Parallel Circuit
The loads are connected “across the line”
  Meaning that they are connected between two conductors that lead to the energy source
The loads and their connecting wires are called Branch Circuits
  All can be called multiple connections and shunt connections
In parallel the loads operate independently
If one branch is disconnected, turned off, or burned open (light bulb) the remaining branches can continue to operate

## Slide 7: Parallel Circuit Example

## Slide 8: Parallel Circuit Example

## Slide 9: Parallel Circuit Example

## Slide 10: Parallel Circuit Voltage and Current
Because the loads are connected across the line the energy source provides the same voltage to the loads
  In series there was voltage drop between the loads
The total current however is distributed among the branches
The amount of current can be found by using Ohm’s Law ( I = V/R )
The lower the resistance is in any branch the greater the current
Lights and small appliances that operates at the same voltage require different amounts of current and is why they would be connected in parallel

## Slide 11: Parallel Resistance Formulas
1/Rt = 1/R1 + 1/R2 + 1/R3 + …
REMEMBER* The total resistance of a parallel circuit is NOT equal to the sum of the resistors

## Slide 12: Parallel Resistance Formulas
Let's summarize this EXAMPLE:
Voltage = 12V
R1 = 4 Ohm
R2 = 4 Ohm
R3 = 2 Ohm

## Slide 13: Parallel Resistance Formulas
1 — = Rt | 1 — + R1 | 1 — + R2 | 1 — R3

## Slide 14: Parallel Resistance Formulas
1 — = Rt | 1 — + 4 | 1 — + 4 | 1 — 2

## Slide 15: Parallel Resistance Formulas
It is easiest to change the fractions into decimal numbers (example 1 divide by 4 equals .25):
1/Rt = .25 + .25 + .5
1/Rt = 1

## Slide 16: Parallel Resistance Formulas
Now you have to get rid of the 1 on the left side so...
Rt = 1/1
Rt = 1 Ohms