## Slide 1: Electronics & Electricity
Unit 3 – Ohms Law
Section 1 – Ohms Law

## Slide 2: Ohms Law
Ohms Law

## Slide 3: Google classroom code
1c62ger

## Slide 4: QUIZ REVIEW
Average grade was a 138.33 out of 150
  92.2 %
  Great job class!
Grades ranged from 90 – 150 points
Only 18 responses of 22
  Be sure to not miss anymore quizzes moving forward

## Slide 20: The big idea
Use the letter symbols for voltage, current, and resistance to show the relationship between them
Calculate the current, voltage, and resistance in a circuit when any two are known quantities
Determine the wattage of an electric circuit when the current and voltage are known
Find the cost of operating an electrical product for a period of time if the cost per kilowatt-hour is known

## Slide 21: Terms
Kilowatt-hour
Ohm’s law
Power
Power formula
Resistance
Watt
Watt-hour meter

## Slide 22: Ohm’s Law
The opposition to the flow of electrons in a circuit is resistance
The law that presents the relationship between voltage, current, and resistance is known as Ohm’s Law
The discovery is credited to George Simon Ohm in 1827
The voltage needed to force a given amount of current is equal to the product of the current and resistance in the circuit
The amount of current in a circuit is equal to the voltage applied to the circuit divided by the resistance of the circuit
The resistance of a circuit is equal to the voltage applied divided by the amount of current

## Slide 23: Ohm’s Law Formulas
Letter symbols
  Voltage (E or V)
  Current (I)
  Resistance (R)
To solve for E (voltage), use the formula:
E = I x R
To solve for I (current), this same formula can be written as:
I = E / R
To solve for R (resistance), arrange it as
R = E / I

## Slide 25: LP 2

## Slide 26: Ohms Law
Letter symbols
  Voltage (E or V)
  Current (I)
  Resistance (R)
To solve for E (voltage), use the formula:
E = I x R
To solve for I (current), this same formula can be written as:
I = E / R
To solve for R (resistance), arrange it as
R = E / I

## Slide 28: Ohm’s Law Practice Worksheet