## Slide 1: Electronics & Electricity
Unit 3 – Ohms Law
Section 2 – Electric and Power

## Slide 2: Electric and Power

## Slide 3: Google classroom code
1c62ger

## Slide 4: The big idea
Use the letter symbols for voltage, current, and resistance to show the relationship between them
Calculate the current, voltage, and resistance in a circuit when any two are known quantities
Determine the wattage of an electric circuit when the current and voltage are known
Find the cost of operating an electrical product for a period of time if the cost per kilowatt-hour is known

## Slide 5: Electric Power and Energy
Power is the time rate of doing work
The basic unit of power is the watt (W)
Named after Scottish inventor James Watt
The watt is based on the unit of work energy, joules per second
Most electrical equipment are rated in terms of power
  60 watt light bulb
  100 watt light bulb
  200 watt light bulb

## Slide 6: Power Formulas
The power formula shows the relationship between electric power (P), voltage (E/V), and current (I) in a circuit
P = V x I

## Slide 7: Power Formulas
Ohm’s law states that V = I x R
By putting I x R in place of V you get
P = I x R x I
= I2R
Also we know I = V/R
By putting V/R in place of I you get
P = V x V/R
= V2 / R

## Slide 8: Power Formula In Use
The basic unit of power is the watt
Problem 1: The current through a 100-ohm resister that is to be used in a circuit is 0.15 A.
  What should be the wattage rating of the resistor?
Solution: Since the two known quantities in this problem are current and resistance, us the formula P = I2R
P = I2R
= .152 x 100
= 2.25 W
In order to keep the resistor from overheating, its wattage rating should be about twice the wattage, about 5 W

## Slide 9: WHY IS THIS IMPORTANT?
Knowing current, voltage, resistance you can safely operate machinery, tools
Assist in knowing how safe the wiring is in your home to apply accessories (stereo, appliances, TVs etc.)

## Slide 10: Power Formula In Use
Problem 2: Find the current that flows through a 60-W incandescent lamp operating at 120 V. Also find the current though a 200-W lamp and a 300-W lamp operating at 120 V.
60-W, 120-V lamp:
I = P / V 60-W / 120-V = 0.5 A
200-W, 120-V lamp:
I = P / V 200-W / 120-V = 1.67 A
300-W, 120-V lamp:
I = P / V 300-W / 120-V = 2.5 A

## Slide 11: LP 2

## Slide 12: Electric and Power

## Slide 13: Weekly Review
Ohm’s law and how to apply the formula
Worksheet for Ohm’s Law practice
Practice soldering testing and fixing
80/20 rule ideation and implementation
New soldering assignment, radio
Next week, Unit 4 - Series-Parallel Circuits

## Slide 14: Electric Power and Energy
Power is the time rate of doing work
The basic unit of power is the watt (W)
Named after Scottish inventor James Watt
The watt is based on the unit of work energy, joules per second
Most electrical equipment are rated in terms of power
  60 watt light bulb
  100 watt light bulb
  200 watt light bulb

## Slide 15: Power Formulas
The power formula shows the relationship between electric power (P), voltage (E/V), and current (I) in a circuit
P = V x I

## Slide 16: Power Formulas
Ohm’s law states that V = I x R
By putting I x R in place of V you get
P = I x R x I
= I2R
Also we know I = V/R
By putting V/R in place of I you get
P = V x V/R
= V2 / R