## Slide 1: Design and drawing for production
Unit 2 – Title Block
Section 2 – Architect Scale

## Slide 2: The big idea
Understand the importance of architect scale usage
Be sure to always identify the scale used
Adding the used scale to our Title Blocks
Using various scales

## Slide 3: Google classroom code
okia9n

## Slide 4: Architect Scale
A triangular shaped instrument used for making or measuring scaled drawings such as blueprints or floor plans.

## Slide 5: Architect Scale
The scale can be read from left to right and right to left.
1/8” scale would be read from left to right and the ¼” scale would be read from right to left.

## Slide 6: Architect Scale

## Slide 7: Drawn to scale?
On a scaled drawing, a small measurement is used to represent a large measurement.
For example, one-fourth inch (¼”) on the plan may represent one foot (1’) in the real world.

## Slide 8: Drawn to scale?
Floor plans for residential structures are usually drawn at ¼” = 1’.
Commercial buildings may be drawn at 1/8” = 1’ if they are too large to fit on the desired sheet size at ¼” = 1’.