## Slide 1: Electronics & Electricity
Unit 3 – Ohms Law
Section 1 – Ohms Law

## Slide 2: Ohms Law
Ohms Law

## Slide 3: Google classroom code
1c62ger

## Slide 4: The big idea
Use the letter symbols for voltage, current, and resistance to show the relationship between them
Calculate the current, voltage, and resistance in a circuit when any two are known quantities
Determine the wattage of an electric circuit when the current and voltage are known
Find the cost of operating an electrical product for a period of time if the cost per kilowatt-hour is known

## Slide 5: Terms
Kilowatt-hour
Ohm’s law
Power
Power formula
Resistance
Watt
Watt-hour meter

## Slide 6: Ohm’s Law
The opposition to the flow of electrons in a circuit is resistance
The law that presents the relationship between voltage, current, and resistance is known as Ohm’s Law
The discovery is credited to George Simon Ohm in 1827
The voltage needed to force a given amount of current is equal to the product of the current and resistance in the circuit
The amount of current in a circuit is equal to the voltage applied to the circuit divided by the resistance of the circuit
The resistance of a circuit is equal to the voltage applied divided by the amount of current

## Slide 7: Ohm’s Law Formulas
Letter symbols
  Voltage (E or V)
  Current (I)
  Resistance (R)
To solve for E (voltage), use the formula:
E = I x R
To solve for I (current), this same formula can be written as:
I = E / R
To solve for R (resistance), arrange it as
R = E / I