## Slide 1: Design and drawing for production
Unit 4 – Alphabet of Lines
Section 1 – Introduction to Alphabet of Lines

## Slide 2: Google classroom code
okia9n

## Slide 3: QUIZ Review
Average grade was 74.29
Grades ranged from 50 to 100
Only 14 submissions out of 25
No longer accepting submissions for the quiz
  Be sure to not miss anymore moving forward

## Slide 14: The big idea
There is an industry standard that has been developed for particular line weights with mechanical drawings
ASME stands for American Society of Mechanical Engineers
Alphabet of Lines reveals shape, size, details and alternate part positions
Different width, darkness, and line types are used to communicate a part

## Slide 16: Visible Lines
Most common used line style
Used to outline the visible edges or contours of the object
Should stand our sharply and be easily noticed
They are the darkest lines in the drawing, besides the border

## Slide 18: Hidden Lines
Indicate edges that cannot be seen by regular view
Thin or medium lines made up of dashes that are evenly spaced
Each dash is about 1/8” while the spacing between each dash is 1/32”

## Slide 20: centerlines
Are thin lines composed of long and short dashes alternately spaced with a long dash at each end
Indicate symmetry
Long dashes are followed by spacing and a short dash

## Slide 22: Construction lines
Very light, gray lines
Used to lay out all work
Should be light enough on a drawing so they will not reproduce or be scene as part of the drawing
If you were an arm length away, you should not be able to see construction lines

## Slide 23: Border lines
Not part of the standard but are used to frame the drawing
Heaviest darkest of the drawing

## Slide 24: LP 2

## Slide 25: Alphabet of Lines
Drawing #8