## Slide 1: Electronics & Electricity
Unit 4 – Series Circuits
Section 1 – Series Circuits

## Slide 2: Series Circuits
Series Circuits

## Slide 3: The big idea
Ability to draw a series circuit, label each part, and identify part’s
Determine voltage drops
Calculate voltage across the circuit

## Slide 4: Terms
Closed loop
Junction
Kirchoffs’ voltage law
Node
Open loop
Polarity
Series circuit
Voltage drop

## Slide 5: Parts of a circuit
An electric circuit is a combination of parts connected to form a complete path through which electrons move
A basic complete circuit has four parts:
The energy source
The conductors
The load
The control device

## Slide 6: The Series Circuit
Is an electrical circuit that has only one path through which electrons can flow

## Slide 7: Example 1

## Slide 8: Example 2

## Slide 9: Example 3

## Slide 10: Open and Closed Loops
Closed Loop is a circuit current can flow
Open loop mean the circuit is incomplete

## Slide 11: Nodes and Junctions
A node is a terminal, connection point between two or more parts of a circuit
Usually identified by LARGE DOTS
Nodes give us a way to say that “wires crossing this junction are connected”
When three or more circuit elements are connected to one point, a junction is formed
Junctions are great testing points for measuring voltage and current

## Slide 12: Polarity
Electrical charge of an energy source
Typically indicated on diagrams by common symbols ( + ) or ( - )
A negative polarity is where current enters a component
A positive polarity is where current leaves a component

## Slide 13: Series Resistance
Because a series circuit has only one path of flow, it must pass through each resistor in a circuit
The total resistance then is the sum of all the resistors in the series circuit
Rt = R1 + R2 + R3 + R4 …..

## Slide 14: Problem 1
Find the total resistance of the three resistors connected in series.
  R1 = 5 Ω
  R2 = 35 Ω
  R3 = 95 Ω
  Rt = R1 + R2 + R3
  Rt = 5 Ω + 35 Ω + 95 Ω
  Rt = 135 Ω

## Slide 15: Problem 2
The same amount of current is available in all parts of a series circuit at any time
A series circuit has a 100-VDC source and three resistors: R1 = 6 Ω, R2 = 12 Ω, R3=7 Ω. Find the total current in the circuit.
Find total resistance
Find total voltage
Utilize Ohm’s Law to calculate total current

## Slide 16: Problem 2 Cont.

## Slide 17: Voltage Drop
Voltage across any load is the amount needed to force the circuit current through resistance of that load
Voltage drop across any load is equal to the current and resistance
Kirchoff’s Voltage Law
  In a series circuit, the sum of the voltage drops across each load is equal to the total voltage applied to the circuit

## Slide 18: Voltage Drop

## Slide 19: Problem 1
The resistance s are connected in series.
Calculate the voltage drop across each resistor
Find total resistance
Calculate the total current
Figure out the voltage drop across each resistor

## Slide 20: Problem 1 Cont.

## Slide 21: Aiding and Opposing Voltage Sources

## Slide 22: Aiding Voltage Sources
Energy sources are often connected in series
Even if the circuit is a parallel and series circuit , the energy source will often still be in series
The series connection affects the total voltage and total current
  Based off of Ohm’s Law
When connected in series the total voltage is equal to the sum of the individual voltages
Batteries are typically connected in the way
Connected so the current flows in the same direction and most of the time if we are using batteries this is the way they are set up.
  Positive terminal of one cell is connected to the negative terminal of the next cell

## Slide 23: Problem 1

## Slide 24: Opposing Voltage Sources
Energy sources sometimes are connected so that the polarity oppose each other
When this happens the voltage opposes each other resulting in a load that is different between the two sources
It has no practical use and is usually avoided
Mentioned here because an inexperienced person may inadvertently connect cells in this way.

## Slide 25: Problem 2

## Slide 26: Schematic Symbols
BATTERY
RESISTOR

## Slide 27: Problem 3
On apiece of paper DRAW a series circuit with
  24-V source
  Four resistors whose sum is 27 Ohms
  At the bottom of your piece of paper answer these questions:
  What is the current in this circuit?
  How many watts does the circuit use?
  Determine the voltage drop across each resistor (R1,R2,R3,R4)